## Slide 1: JCUSI
ARTIGO
SOFTWARE ARCHITECTURE

## Slide 2: ARTIGO Applications
packbot_node
  Purpose: Provides an interface to the robot
  Receives: Actuator control commands that are published from the ROS node called commander_node
  Provides: Robot sensor data and robot state information using the AWARE2 API and iRobot Third Party Protocol
  Source code language: C++
  Source code location: jcusi_artigo/src/
  Executable location: jcusi_artigo/bin/packbot_node
commander_node
  Purpose: Provides the intelligent behavior on the robot
  Receives:
    Laser range finder data from the laser_publisher node
    Magnetic headings from the compass_publisher node
    Lattitude and Longitude from the gps_publisher node
    Receives mission commands from the SCC using an established socket
    When in manual mode, receives manual control commands from the SCC using the established socket
  Provides: Publishes actuator commands that control the robot
  Source code language: Python
  Source/Executable code location: jcusi_artigo/src/commander_node.py

## Slide 3: ARTIGO Applications Continued
gps_publisher
  Purpose: Publish latitude and longitude acquired from the GPS
  Receives: NMEA string from gpsd at baud rate of 9600 (gpsd automatically negotiates this and may change it, you can find the baud rate by typing: stty –F /dev/ttyUSB0)
  Provides: Publishes the GPS data as ros messages:
    fix
    extended_fix
  Source code language: Python
  Source/Executable code location: jcusi_artigo/src/gps_publisher.py
  External Requirement: gpsd must be installed . The gps-umd package which includes gpsd client needs to be installedw
hokuyo_node (laser range finder)
  Purpose: Publish the ranges in meters returned from the laser range finders (LRF)
  Receives: An array of range readings from the LRF (see LRF documentation)
  Provides: Publishes the LRF data as ros messages:
    diagnostics
    hokuyo_node/parameter_descriptions
    hokuyo_node/parameter_updates
    Scan
  Source/Executable code location: In the hokuyo_node stack of ROS
  External Requirement: Hokuyo ROS Stack installed
compass_publisher
  Purpose: Publish the heading from the compass
  Receives: The heading, pitch, roll, and temperature from the compass
  Provides: Publishes the heading data as ros message:
    compass_msg
  Source code language: Python
  Source/Executable code location: jcusi_artigo/src/compass_publisher.py

## Slide 4: ARTIGO Software Diagram
extended_fix
ARTIGO
SCC
Two way communication
over TCP Sockets
Medium: Wireless Radio (4.9 ghz)
gpsd_client
hokuyo_node
(Laser Range Finder)
compass_node
scan
compass_msg
commander_node
packbot_node
robot_state
robot_commands
Packbot
Two way communication
Using AWARE2 Session
Medium: Wired (CAT 5)
node
message
………. A ROS Message
………. A ROS Node